## Slide 1: Unstructured Wave Modeling in E3SM
Steven Brus, Phillip J. Wolfram, Jon Wolfe, Andrew Roberts, Elizabeth Hunke, Qing Li, Luke Van Roekel, & the E3SM community
E3SM Coastal Waves NGD

## Slide 2: Role of Waves in the Coupled Climate System
Cavaleri et al. (2012)
Wind-generated waves are an important interfacial process in the climate system
Some cross-component interactions include:
  Ocean vertical mixing
  Sea-state dependent drag
  White-capping albedo
  Sea-ice floe size

## Slide 3: Role of Waves in Coastal Flooding
Melet et al. (2018)
Climate drivers
(Storms)
Kerr et al. (2013)
Wave contribution to water levels during Hurricane Ike
Maximum water level difference

## Slide 4: Trend in Global Wave Climate
Young et al. Science (2011)
Global wave (and wind) extremes have been increasing
Especially at high latitudes

## Slide 5: Wave Energy Spectrum
Wind waves represent a distinct portion of the energy spectrum
Wavelengths order 10-100 m
Periods order 1-10s
Require separate modeling approach
Phase averaged paradigm vs. directly modeling sea surface

## Slide 6: Spectral Description of Waves
Image Credit: ECMWF
Actual water surface represented by summation of sinusoidal components with different frequencies and directions
Spectrum: Distribution of energy among the components
Image Credit: ECMWF

## Slide 7: Spectral (Phase-Average) Wave Modeling
- Atmosphere-wave interaction
- Dissipation
- Non-linear wave interactions
- Triad interactions
- Wave scattering
- Wave-bottom interactions
- Depth-limited breaking
- Wave-ice interactions
- Reflection
Advection by group velocity and currents
Frequency dispersion
(stretching)
Refraction
(bending)
Production,
Dissipation,
Non-linearities
Describes evolution of action density:
lon
lat
relative
fequency
direction
time
energy density

## Slide 8: Mean Wave Parameters
Significant Wave Height
Mean Wave Period
Mean Wave Direction
Image credit: Motion Forecasting

## Slide 9: Global Wave Spectra ML Classification
Wave spectrum clusters
Correlation Coefficient
Representative cluster wave spectra

## Slide 10: WaveWatchIII Mesh Configurations
Current operational WWIII nesting
Spherical Multi Cell WWIII grid
Regional Triangular Mesh
Chawla et al. (2013)
Li (2012)
Abdolali et al. (2020)

## Slide 11: Integration of WaveWatchIII into E3SM
WaveWatchIII is now available via GitHub: https://github.com/NOAA-EMC/WW3
Latest version 6.07 has been made a submodule in E3SM
WaveWatchIII uses “switches” to define physics/formulation options. Source code must be pre-processed to generate compliable code.
Several auxiliary programs are necessary for processing grids, initial conditions, and output

## Slide 12: Importance of Regional Refinement
Shallower (coastal):
Requires higher resolution
Deeper (open ocean):
Accurate with
lower resolution
Structured lon-lat meshes
June-August 2005 CFSR winds
Comparison with NDBC buoys

## Slide 13: Global Unstructured WaveWatchIII Meshes
Quasi-uniform 50 km
Regionally Refined Delaware Bay
240km – 4km
Meshes generated with OceanMesh2D software:
https://github.com/CHLNDDEV/OceanMesh2D

## Slide 14: Global Unstructured Mesh Validation
100km unstructured
50km unstructured
½o structured
Observed
June-August 2005
CFSR winds (1/2 degree resolution)
Comparison with NDBC buoy data

## Slide 15: Global Unstructured Mesh Validation
June-August 2005
CFSR winds (1/2 degree resolution)
Comparison with NDBC buoy data
100km unstructured
50km unstructured
½o structured
Observed

## Slide 16: Global Unstructured Mesh Validation
June-August 2005
CFSR winds (1/2 degree resolution)
Comparison with NDBC buoy data
100km unstructured
50km unstructured
½o structured
Observed

## Slide 17: Global Unstructured Mesh Validation
June-August 2005
CFSR winds (1/2 degree resolution)
Comparison with NDBC buoy data
100km unstructured
50km unstructured
½o structured
Observed

## Slide 18: Global Regionally Refined Mesh Validation
½o structured
Observed
4km unstructured
2km unstructured
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data
4km unstructured
14x faster than
1/2o structured

## Slide 19: Global Regionally Refined Mesh Validation
4km unstructured
2km unstructured
Observed
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data
½o structured
Observed
4km unstructured
2km unstructured
4km unstructured
14x faster than
1/2o structured

## Slide 20: Global Regionally Refined Mesh Validation
4km unstructured
2km unstructured
Observed
½o structured
Observed
4km unstructured
2km unstructured
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data
4km unstructured
14x faster than
1/2o structured

## Slide 21: WaveWatchIII Coupler Mapping
WaveWatchIII already uses SCRIP internally for mapping nested grids
Repurposed for generating mapping files for E3SM
ww3_grid
mod_def.ww3
mesh.msh
ww3_grid.inp
wave_scrip_file.nc
E3SM
ESMF_RegridWeightGen
map_file.nc
other_scrip_file.nc
Image Source: WaveWatchIII User’s Manual

## Slide 22: Data Atmosphere + Unstructured Waves Compset
E3SM: datm+WWIII
WWIII Standalone
Observed
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data

## Slide 23: Data Atmosphere + Unstructured Waves Compset
E3SM: datm+WWIII
WWIII Standalone
Observed
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data

## Slide 24: Data Atmosphere + Unstructured Waves Compset
E3SM: datm+WWIII
WWIII Standalone
Observed
Hurricane Sandy 2012
CFSv2 winds (0.2 degree resolution)
Comparison with NDBC buoy data

## Slide 25: Summary
Next Steps
Performance evaluation of global unstructured configuration
One-way coupling from ocean and sea-ice to waves (verification)
Two-way coupling between waves, ocean, and sea ice (G case+waves)
Collaborate with InterFACE project on wave/ice couplings and simulations
Waves are an important interfacial process in the climate system
High latitude wave heights are increasing
E3SM will have the first coupled, global unstructured WaveWatchIII configuration
Our initial validation results have shown promise in balancing accuracy and cost