## Slide 1: Land River Two-Way Coupling Development in E3SM
Donghui Xu1, Gautam Bisht1, Tian Zhou1,
Chang Liao1, Hong-Yi Li2, Zeli Tan1
ICoM is funded by multiple programs in the Earth and Environmental Systems Sciences Division of DOE’s Office of Science
2020 ESMD-E3SM PI meeting
1Pacific Northwest National Laboratory
2University of Houston
October 26, 2020

## Slide 2: Land-river-ocean three-way coupling in E3SM
ELM
MOSART
MPAS-O
Notes: Combine this one and configuration

## Slide 3: Proposed Two-Way Coupling Scheme
Inundation Fraction, Inundation Volume
ELM
MOSART
Infiltration on Floodplain
ICoM proposed developments
Ongoing E3SM developments
Test simulation configuration
Global
COMPSET = IELM (ELM+MOSART)
QIAN atm forcing
Kinematic wave routing
Inundation is turned on
Water management is turned off
Simulation period: 1951-1970
  First 15 year is used as “spin up”
  Last 5 year is used to show comparison
Notes: Combine this one and configuration

## Slide 4: Comparison Between Two-Way and One-Way
Results of a single cell during a rainfall event
Higher surface runoff
Higher subsurface runoff
Wetter Soil
Two-way coupling has
Less floodplain inundation
Notes: Subsurface runoff, replace the channel volume. Water table comparison

## Slide 5: Comparison of Peak Runoff at Global Scale
13% cells with increase at least 5%
2% cells with decrease at least 5%
-
[-]
[days]
17.6% cells the peak runoff doesn’t occur on the same day between two-way and one-way
Notes: Time series daily scale
Max daily runoff

## Slide 6
Magnitude Timing | Higher | Same | Lower
Earlier | 4% | 0 | 2.4%
Same day | 37.7% | 11.6% | 31.7%
Later | 6.5% | 0 | 2%
Notes: Time series at daily for each example

## Slide 7: Calibration
Previous study calibrated for the inundation faction by tunning river depth and width, but result in unrealistic parameters.
GIEMS
Current river depth
Notes: Zoom in plot

## Slide 8: Calibration
Previous study calibrated for the inundation faction by tunning river depth and width, but result in unrealistic parameters.
GIEMS
Current river depth
Notes: Zoom in plot

## Slide 9: Calibration: ongoing process
Estimate river width and depth based on [Andreadis et al., 2013]:
(is the 2-year return period annual peak discharge)
Keep and fixed, and calibrate elevation profile with a satellite inundation product (GIEMS).
More Inundation
Less Inundation
[m]
Step 1 - calibrate discharge
Step 2 - calibrate inundation
Notes: Show giem inundation